## Slide 1: 2025 Nevada Transportation Conference
May 14, 2025
I-80 East Vista to USA Parkway Widening Project

## Slide 2: Project Area
Interstate 80 (I-80): Vista Boulevard to USA Parkway
Interchanges:
  Mustang
  Patrick
  Lockwood including UPRR bridge
  USA Parkway
  Vista Blvd.

## Slide 3: Critical Project Elements
Widening inside shoulders to 10’
Widening outside shoulders to 12’
Constructing median barrier rail
Upgrading guard rail to concrete barrier rail
Wrong way driver detection
Safety Elements
Additional lane in each direction
Interchange improvements
Traffic Elements
Statewide Crash Rate Comparison | Total Crashes | PDO | Injury | Injury (Type A) | Fatal | Fatalities
Vista to 0.95 miles east of Mustang (Urban) |  |  |  |  |  | 
0.95 mile east of Mustang to USA Pkwy (Rural) |  |  |  |  |  | 
- Corridor exceeds statewide crash rate
PDO – Property Damage Only
Injury (Type A) refers to incapacitating injuries with potential lifelong injuries
2050 Forecasted Volumes
Westbound
    3,580 vehicle per hour (PM peak period)
    Eastbound
    3,059 vehicles per hour (PM peak period)
Notes: TRIC generates 40,000 VPD in 2050 per RTC model

## Slide 4: Concept Development and Project Area Constraints
Mountainous terrain elements
Truckee River, UPRR, and Areas of Environmental Concern
Temporary and permanent water quality improvements
Truckee River
UPRR
Multiple Environmental Avoidance Areas
Mountainous
Terrain
Mountainous
Terrain
Temporary and Permanent Water Quality
Cooling Ponds

## Slide 6: Proposed Build Alternative
Roadway Section
Travel lanes – Three lanes, 12 feet each direction
Inside shoulder – 10 feet
Outside shoulder – 12 feet
Roadway Elevation
Match existing roadway elevations
Raise or lower roadway elevations to minimize impacts
Alternatives are preliminary and subject to change
Existing Slope
Proposed Slope
Proposed Retaining Wall

## Slide 7: Key Construction Elements and Risks
Substantial slope cuts and walls
  More complex walls – soil nail/rock anchors on north side
  Also occurs west of Patrick
Center median wall for a majority of the corridor
  Potential construction impacts and additional costs due to proximity to existing/future lanes based on phasing
Drainage
  Cross roadway connectivity – phasing challenges
  Water quality facilities
Maintenance of Traffic
  Increasing traffic volumes

## Slide 8: Project Status
NEPA completion anticipated summer 2025
NDOT awarded $275 million INFRA grant for project
  $25M pre-construction activities
  $250M construction activities
Project development
  Program manager procurement
  Interim Geotechnical investigation
  Progressive Design Build (PDB)

## Slide 9: Project Schedule
Key Milestone – September 2027 INFRA Grant Obligation Deadline

## Slide 10
Thank You!
I80eastnv.com
Chris Kuhn – NDOT Project Manager
ckuhn@dot.nv.gov
(775) 888-7728